## Slide 1
COMPLEX ENGINEERING PROJECT (CEP) REPORT
Battery Health Prediction and Remaining Useful Life Estimation Using Machine Learning
Rabeea Anjum
Roll No. 23CSE09
Supervised by Dr. Muhammad Bux Alvi
Department of Computer Systems Engineering | Faculty of Engineering & Technology
The Islamia University of Bahawalpur

## Slide 2
ABSTRACT
An ML-Based Approach to Battery Degradation
Lithium-ion batteries are the backbone of modern energy storage — from electric vehicles to consumer electronics and renewable-energy storage — but their performance degrades progressively with repeated charge-discharge cycling.
This project proposes a machine learning-based Battery Management System (BMS) that predicts two targets simultaneously: State of Health (SOH) and Remaining Useful Life (RUL).
Predictions are based on seven operational parameters: charging current, charging voltage, charging temperature, discharging current, discharging voltage, discharging temperature, and number of cycles.
The methodology combines Exploratory Data Analysis, IQR-based outlier detection, feature engineering, StandardScaler normalization, and a Random Forest multi-output regression model trained on real cycling data from NASA battery cells B5, B6, and B7.
The trained model showed good predictive performance, suitable for intelligent battery analytics and real-time BMS use cases.
95.19%
of predictive feature importance comes from cycle count alone
3 NASA battery cells (B5, B6, B7) across hundreds of charge-discharge cycles
Battery Health Prediction & RUL Estimation — CEP Report
1

## Slide 3
INTRODUCTION
Why Battery Health Matters
Lithium-ion batteries are a strategic player in modern engineering, driving the fast global growth of electric vehicles, portable electronics, and grid-scale energy storage.
Compared with other chemistries, these electrochemical cells offer high energy density, low self-discharge, and long cycle life.
Performance inevitably deteriorates through complex electrochemical processes: lithium plating, solid-electrolyte interphase (SEI) layer formation, loss of active electrode material, and structural fatigue of the electrode lattice.
Left unmonitored, this degradation can cause unexpected capacity failure and rising internal resistance — and in extreme cases, thermal runaway events that pose a serious safety risk.
Electric Vehicles
Consumer Electronics
Renewable Energy Storage
Unmonitored degradation risks thermal runaway — a critical safety concern.
Battery Health Prediction & RUL Estimation — CEP Report
2

## Slide 4
INTRODUCTION
From Lab Models to Data-Driven Learning
Traditional BMS
Built on electrochemical models or look-up-table approaches to estimate battery health.
Effective in controlled laboratory conditions.
Weaker at handling real-world variability — operating temperature, load patterns, and manufacturing tolerances across individual cells.
Data-Driven Machine Learning
Offers an excellent alternative — or augmenting tool — to physics-based models.
Learns highly nonlinear degradation behaviour directly from operational data.
Forms the basis of the multi-output Random Forest approach used in this project.
Battery Health Prediction & RUL Estimation — CEP Report
3

## Slide 5
PROJECT OVERVIEW
An Intelligent System for Degradation Analysis
This project implements a Battery Management System that analyses degradation using machine learning, predicting State of Health and Remaining Useful Life from seven operational parameters.
OPERATIONAL INPUTS
Charging current
Charging voltage
Charging temperature
Discharging current
Discharging voltage
Discharging temperature
Cycle count
Random Forest
Multi-Output
Regression Model
PREDICTED OUTPUTS
State of Health (SOH)
Battery capacity ratio
Remaining Useful Life (RUL)
Cycles remaining
Toward smart battery degradation prediction & lifecycle management.
Exploratory Data Analysis
Feature Engineering
Feature Scaling
Multi-Output Regression
Random Forest Regression
Battery Health Prediction & RUL Estimation — CEP Report
4

## Slide 6
OBJECTIVES
Project Objectives
1
Predict the health of lithium-ion batteries over charging cycles.
2
Make accurate estimation of battery Remaining Useful Life (RUL).
3
Interpret patterns of thermal and electrical behaviour.
4
Analyze degradation of different battery cells.
5
Create a smart, AI-based data analytics system that can be integrated with a BMS.
Battery Health Prediction & RUL Estimation — CEP Report
5

## Slide 7
DATASET
Dataset Description
Sourced from the NASA Ames Prognostics Data Repository: lithium-ion battery operation across many charge-discharge cycles for three battery cells — B5, B6, and B7 — with eight electrical and thermal parameters recorded per cycle.
INPUT FEATURES
Feature | Description
battery_id | Battery identifier (B5, B6, B7)
Cycle | Charge-discharge cycle number
chI | Charging current (Amperes)
chV | Charging voltage (Volts)
chT | Charging temperature (°C)
disI | Discharging current (Amperes)
disV | Discharging voltage (Volts)
disT | Discharging temperature (°C)
TARGET VARIABLES
Target | Description
SOH | State of Health (battery capacity ratio)
RUL | Remaining Useful Life (cycles remaining)
Battery Cells Studied
B5
B6
B7
Hundreds of charge-discharge cycles per cell provide a real-world basis for SOH and RUL modelling.
Battery Health Prediction & RUL Estimation — CEP Report
6

## Slide 8
METHODOLOGY
End-to-End Machine Learning Pipeline
1
Load Dataset
2
Check Missing
Values
3
Label Encoding
4
Exploratory
Data Analysis
5
Outlier Detection
(IQR)
6
Feature
Engineering
7
Feature Scaling
8
Train-Test Split
(80 / 20)
9
Train Random
Forest Model
10
Model
Evaluation
11
Feature Importance
Analysis
Implemented end-to-end in Python (pandas, NumPy, scikit-learn, seaborn) within Google Colab.
Battery Health Prediction & RUL Estimation — CEP Report
7

## Slide 9
EXPLORATORY DATA ANALYSIS
Understanding the Data Before Modelling
Correlation Heatmap
Visualizes relationships among all numerical variables using a Seaborn heatmap, highlighting which parameters move together.
Cycle vs. State of Health
Line plots of SOH against cycle number for each battery reveal a consistent degradation trend as cycling continues.
Cycle vs. Remaining Useful Life
Line plots show RUL steadily decreasing as the battery accumulates more charge-discharge cycles.
Temperature & Battery Type vs. SOH
A regression plot examines charging temperature against SOH, while a boxplot compares SOH distribution across battery_id.
Battery Health Prediction & RUL Estimation — CEP Report
8

## Slide 10
DATA QUALITY
Outlier Detection — IQR Method
A non-parametric Interquartile Range (IQR) method was used to flag extreme values — a robust approach for sensor data.
Applied to the key numerical columns: Battery Charging Time (BCt), SOH, and RUL.
For each column: Q1 (25th percentile) and Q3 (75th percentile) are computed, and IQR = Q3 − Q1.
Values falling below Q1 − 1.5×IQR or above Q3 + 1.5×IQR are flagged as outliers.
Boxplots were used to visualize the spread and distribution of each column before formal IQR screening.
Boxplot Visualization
BCt · SOH · RUL examined individually to check spread, skew, and possible extreme values.
No Significant Outliers Found
The NASA dataset's numerical features passed IQR screening cleanly, confirming good data quality before modelling.
Battery Health Prediction & RUL Estimation — CEP Report
9

## Slide 11
FEATURE ENGINEERING
Capturing Differential Stress Signals
Three new engineered features were derived from the raw electrical and thermal readings, capturing differential conditions during charging and discharging — well-known indicators of battery degradation.
Voltage_Diff
chV − disV
Differential voltage between charging and discharging phases.
Temp_Diff
chT − disT
Differential thermal response across charge / discharge.
Current_Diff
chI − disI
Differential current draw between charging and discharging.
Battery Health Prediction & RUL Estimation — CEP Report
10

## Slide 12
PRE-PROCESSING
Feature Scaling & Train-Test Split
Feature Scaling
Feature magnitudes normalised to zero mean and unit variance using Scikit-Learn's StandardScaler.
Ensemble tree-based models like Random Forest don't typically need scaling.
Applied anyway as part of a professional preprocessing pipeline — for reproducibility and to support future comparisons with distance- or gradient-based models.
Train-Test Split
Chart: 
| Training (80%) | Testing (20%)
Split | 80 | 20
Training: 80%
Testing: 20%
Fixed random_state = 42 ensures reproducible splits across runs.
Battery Health Prediction & RUL Estimation — CEP Report
11

## Slide 13
MACHINE LEARNING MODEL
Random Forest Regressor
A multi-output ensemble regression model — RandomForestRegressor — was chosen for this study. During training it builds many decision trees and averages their predictions, giving robust and interpretable performance widely applied in battery health prediction tasks.
Model Configuration
n_estimators
200
random_state
42
WHY RANDOM FOREST?
Handles non-linear relationships among features and targets.
Works well with tabular sensor data.
Natively supports multi-output regression.
Easy to interpret the results.
Comes with built-in feature importance.
Battery Health Prediction & RUL Estimation — CEP Report
12

## Slide 14
MODEL EVALUATION
Assessing Multi-Output Prediction Performance
MAE
Mean Absolute Error
Average magnitude of prediction errors.
MSE
Mean Squared Error
Penalizes larger errors more heavily.
RMSE
Root Mean Squared Error
Interpretable in the original units.
R²
R² Score
Proportion of variance explained by the model.
Actual-vs-Predicted plots were generated for both SOH and RUL, visually confirming how closely model predictions track the true values on the held-out test set.
Battery Health Prediction & RUL Estimation — CEP Report
13

## Slide 15
KEY FINDING
Feature Importance Analysis
Chart: 
| Cycle | battery_id | Others (Voltage, Temp, Current, etc.)
Importance (%) | 95.19 | 4.6 | 0.21
Feature importance in Random Forest is derived from the mean decrease in impurity (MDI) across all trees — a transparent, model-internal measure of relevance.
Cycle count drives 95.19% of predictive importance — far ahead of battery_id (4.60%) and all other measured signals (< 0.21%).
This mirrors findings reported by Severson et al. and Nuhic et al. in independent battery prognostics studies.
It is consistent with the electrochemical understanding that SEI layer formation and lithium plating are inherently cycle-dependent.
Wang et al. similarly identified cycle number as the principal driver of capacity reduction, using relevance vector machines.
Battery Health Prediction & RUL Estimation — CEP Report
14

## Slide 16
RESULTS
Key Insights
Degradation Patterns
Battery health declines as cycling continues.
RUL continuously decreases as batteries age.
Degradation is shaped by multiple stresses; temperature is not the dominant factor in this dataset.
Cycle count is the most reliable predictor of degradation (~95%).
Degradation behaviour differs across battery cells B5, B6, and B7.
Modelling Outcomes
Engineered features (Voltage_Diff, Temp_Diff, Current_Diff) aided dataset understanding.
No significant outliers were found in the data.
Random Forest produced good multi-output regression results across all targets.
The model can be integrated into intelligent Battery Management Systems.
Professional ML preprocessing best practices (scaling) were followed.
Battery Health Prediction & RUL Estimation — CEP Report
15

## Slide 17
LOOKING AHEAD
Future Work
Apply LSTM and GRU deep learning models for temporal sequence modelling.
Develop a real-time, IoT-based Battery Management System for live monitoring.
Expand the dataset to cover a wider range of thermal operating conditions.
Optimize closed-loop fast-charging protocols using machine learning.
Add monitoring alerts (e.g. email) triggered once batteries reach critical levels.
Explore chemistry-dependent voltage signature analysis.
Apply Sequential Monte Carlo (SMC) / MCMC methods for RUL estimation.
Battery Health Prediction & RUL Estimation — CEP Report
16

## Slide 18
TECHNOLOGY STACK
Technologies Used
Python
Primary programming language
Pandas
Data loading, manipulation & analysis
NumPy
Numerical computation
Matplotlib
Data visualization & plotting
Seaborn
Statistical data visualization
Scikit-Learn
Preprocessing, modelling & evaluation
Google Colab
Cloud-based development & execution
Battery Health Prediction & RUL Estimation — CEP Report
17

## Slide 19
CONCLUSION
A Validated, Deployable Approach to Battery Health Prediction
The Random Forest multi-output regression model successfully predicted both SOH and RUL using real NASA lithium-ion cycling data from cells B5, B6, and B7.
Cycle count emerged as the dominant predictor of degradation, accounting for ~95.19% of feature importance.
Low prediction error and a high R² score demonstrate the model's ability to generalize across different battery cells.
The resulting system is suitable for deployment in intelligent battery analytics and real-time Battery Management System (BMS) applications.
Thank You
Rabeea Anjum (23CSE09) · Supervised by Dr. Muhammad Bux Alvi
Department of Computer Systems Engineering, The Islamia University of Bahawalpur